## Slide 1: Noise performance of microwave humidity sounders over their life time Imke Hans Universität Hamburg
Imke Hans1, Martin Burgdorf1, Viju O. John2,3, Jonathan Mittaz4,5, and Stefan A. Buehler1
1 Meteorologisches Institut, Centrum für Erdsystem- und Nachhaltigkeitsforschung (CEN), Universität Hamburg
2 EUMETSAT, Darmstadt
3 Met Office Hadley Centre, Exeter, United Kingdom
4 Department of Meteorology, University of Reading, Reading, UK
5 National Physical Laboratory, Teddington, UK

## Slide 2: Motivation
How does the noise of the MW instruments SSMT2, AMSUB and MHS
evolve over their life time?
New aspects in
Noise: Definition and calculation using Allan Deviation
MW instruments: individual instruments of SSMT2, AMSUB, MHS on all platforms
Evolution: assessment over whole life time
 goals
  overview of usable data
  insight to known issue
  input for uncertainty budget of new FIDUCEO FCDR

## Slide 3: Outline
Method: Noise definition and calculation
Main results
  Noise Evolution and usable data
  Insight to known issue: AMSU-B N16 bias vs other instruments
  Input for uncertainty budget in FCDR
Conclusions

## Slide 4: 1. Method
Noise definition
“count noise”: Fluctuations in instrumental counts:
  Deep space view (DSV)
  View of the internal warm calibration target (IWCT)
Noise Equivalent Differential Temperature (NEdT)
  From DSV counts: “cold NEdT”
  From IWCT counts: “warm NEdT”
  Rescaling to “scene NEdT”
Noise calculation
Allan Deviation: inter-scanline-wise, on each calibration view
Advantage: not sensitive to orbital variations
Scaling of count noise to Temperature NEdT

## Slide 5: 2.a. Noise evolution and usable data
DSV Count noise
Cold NEdT
Behaviour of Count noise and NEdT:
  Changes in count noise  changes in NEdT
  But: NEdT also reflects changes in gain
Evolution different for instruments and channels
  e.g. strong degradation of NOAA15, 16 in Ch3 NEdT
  on METOP-B: Very stable count noise and NEdT

## Slide 6: 2.a. Noise evolution and usable data
Usable data:
e.g. NEdT <1K
Periods of cold NEdT < 1 K
 “quick look” overview of noise and NEdT for all instruments and channels
For NEdT <1K: time series for all channels without gaps may be constructed

## Slide 7: 2.b. Insight to N16 bias
Bias N16 vs MHS N18 (yellow) increases dramatically…
…so does NEdT (green)
…because of the decreasing gain
RFI has more impact  likely to cause the bias

## Slide 8: 2.c. Input for uncertainty budget in FIDUCEO FCDR
Count noise estimation (Allan Dev.) applied in FCDR processing
DSV, IWCT, scene count noise estimated on-the-fly
Propagated to brightness temperature Tb
 “uncertainty in Tb due to noise on scene counts” on pixel level

## Slide 9: 3. Conclusions
We have used: Allan Deviation (not sensitive to orbital variations) for estimating count noise and NEdT
We provide: Overview of count noise and NEdT evolution over life time of all individual SSMT2, AMSUB, MHS instruments
We suggest: RFI as possible explanation for AMSUB N16 bias
We provide: input for uncertainty budget of FIDUCEO MW FCDR which we work on

## Slide 10
Thank you!

## Slide 11: Back up slides

## Slide 12: Scene NEdT
Rescaling for scene NEdT

## Slide 13: Gain decrease - evolution of counts Channel 3 AMSUB NOAA16

## Slide 14: Gain decrease - evolution of counts Channel 3 MHS NOAA19

## Slide 15: DSV count noise spectrum
Noise spectrum calculated with bias function
Ch2 has pink noise component
Ch3 has stronger pink noise component in 2006 than in 2003

## Slide 16: DSV count noise
Ch2: inter-pixel-method too low
Ch3: in 2006, when pink noise stronger, inter-pixel-method too low