## Slide 1: Consistent Data Records From Microwave Sounders
I. Hans, T. Lang, S. A. Buehler, M. J. Burgdorf, M. Prange
FIDUCEO has received funding from the European Union’s Horizon 2020 Programme for Research and Innovation, under Grant Agreement no. 638822

## Slide 2: Consistent Data Records From Microwave Sounders
I. Hans, T. Lang, S. A. Buehler, M. J. Burgdorf, M. Prange
FIDUCEO has received funding from the European Union’s Horizon 2020 Programme for Research and Innovation, under Grant Agreement no. 638822

## Slide 4: Microwave humidity sounding Advanced microwave sounding unit - b Special sensor Microwave - humidity
Fiduceo microwave easy fcdr

## Slide 5: What is New? Features of FIDUCEO FCDR & Example Contents
Data format: NetCDF
  Easy to use
  Attributes explaining the variables
Data arrangement: equator – to – equator
On pixel-level:
  Brightness temperatures for channels
  Uncertainties due to independent, structured, and common effects
  Quality information
Improved antenna pattern and radio frequency interference corr.
Information on transmitter status in bitmask for scan line quality (helpful for RFI related issues)
Per scan line: original scan line number and file (level 1b)

## Slide 6: Uncertainties: Relative Importance
Histogram of the three classes of uncertainties:
September 2014
MHS on Metop-B
Similar pattern for the three sounding channels
Long tail for common effects in channel 1 due to antenna pattern correction
Except for channel 1, the independent uncertainties dominate the others

## Slide 7: Comparison of Tb From AAPP/Fiduceo, Channel 3
The FCDR from FIDUCEO provides more consistent and stable time series
The shaded regions denote the uncertainty due to common effects for FIDUCEO
There is no uncertainty estimate on pixel level for the products of AAPP

## Slide 8: upper tropospheric humidity cdr

## Slide 9: A New Definition of UTH and New CDR Content
CDR content:
  Monthly averages of UTH and BT in the tropics
  Regular lat/lon grid
  1°×1° resolution
  Separate data fields for ascending and descending overpasses
  Uncertainty information
Uncertainties for UTH and BT propagated from FCDRs
Correlations between individual pixels lead to correlations between the individual grid cell average
Idea: UTH = vertical average of RH in an IWV layer (defined by Wu et al., 1993)
Advantages: Same definition for IR and MW with same thresholds, value follows directly from model atm.

## Slide 10: Example CDR Content
UTH + Uncertainties
BT + Uncertainties
July 2012 from ascending passes of MHS on NOAA18

## Slide 11: Inter-calibration of microwave sounders

## Slide 12: Opportunistic Constant Target Matchups - Methodology
Basic idea:
  Instead of temporal matching, SEVIRI radiance (6.2 μm) has to match.
Complements SAACs very well.
Mitigates effect of diurnal cycle on inter-calibration that is present with averaging methods.
SEVIRI (geostationary)
4.5 h apart

## Slide 13: The Moon as Microwave Calibration Reference
Check Pointing, Beam Size, and Sounding Channel Uniformity in Flight
Check Photometric Stability With TB = f(φ) and Hundreds of Moon Intrusions in DSV

## Slide 14: Conclusions
FCDRs for all channels of MHS, AMSU-B, SSM/T-2
    Consistent calibration resulted in significant reduction of bias
Upper tropospheric humidity calculated from FCDRs
    Uncertainties propagated from FCDR to CDR
    Binning to Lat/Lon grid and monthly averages
Characterization of instrumental effects and noise => user-friendly set of TB and UTH for the period 1994 – 2017
FIDUCEO has received funding from the European Union’s Horizon 2020 Programme for Research and Innovation, under Grant Agreement no. 638822